BARKLEY COMMUNITY LIMITED PARTNERSHIP

PO BOX 759

UCLUELET, BC

V0R 3A0

May 8, 2018

Attention:	To Whom It May Concern

Re: Road Permit Package for Tender R21331 2018-01 Barkley Community Limited Partnership

Licence K3S

Barkley Community Limited Partnership is accepting proposals for the road construction listed below to access Cut blocks OZ 3 in Licence K3S Road Permit R21331.

The following roads total a length of 3498 meters

- M100A              0+000-2+598-Reconstruction

- M100B              0+000-0+193- Reconstruction

- M100C              0+000-0+244- Reconstruction

- M100C              0+244-0+311- New Construction

- M100K              0+000-0+396- New Construction

Your proposal (quote) should consider the flowing conditions:

- You will accept the  role of prime contractor and are qualified to take on the role of prime in a multi- employer work site

- Provide WBC clearance letter

- Provide liability insurance in the amount of a minimum $5,000,000

- Provide First Aid coverage per WBC Regulation Section 3

- Construct all roads, culverts, WBC and bridges to the RDL, profiles, Road Construction maps, Bridge Designs, Preworks, Fish reports and the Environmental Sediment  Management Plan

- Roads and bridges, WBC should be constructed for L 100 load ratings with a minimum 5 meter running surface and adequate ballast material (0.3m) for these roads.

- Pay all costs to mob/demob equipment to and from site

- Provide all necessary equipment, personal and supplies (culverts, geotextile, hay bales, staples) to complete the roads as per the signed contract

- Provide a list of equipment with hourly rates and employees experience and training to complete the job

- List road construction completed to date with references

- List potential local contractors or First Nation’s that can be hired as sub-contractors or employees for this job. Local employment is an important item with this contract and your proposal.

- Barkley Community Tenure will provide R/W fallers and pay for this cost

- Barkley Community Tenure will provide and pay for the 12m steel portable bridge and deliver to the start of the site from which the contractor must install.

- Provide a total dollar lump sum to construct the roads

Please submit your sealed proposal in writing with your all found lump sum to construct the roads listed in this package by June 1, 2018 to:

Zoltan Schafer, RPF

Barkley Community Tenure Manager

2859 Carmichael Crescent

Port Alberni, BC

V9Y 7V5

The BCFLP makes no commitments as a result of this road proposal and may, as a result of submissions received, accept or reject a bid at their sole discretion. Based on the proposals received, the BCFLP may issue a road construction contract and prime contractor agreement for the roads to be constructed in this proposal.

For further information please contact the undersigned in Port Alberni.

Yours truly,

Zoltan Schafer, RPF

Forestry Manager

Barkley Community Tenure

250-720-1177

zolie_schafer@telus.net